SET-UP INSTRUCTIONS FOR BACKUP GPS-LOGGERS

MAIN MENU - SETUP:

- SYSTEM or GENERAL

    - Make sure WAAS is enabled

- UNITS or LOCATION

    - Position Format – UTM UPS

    - Map Datum – NAD 27 CONUS

- TIME

    - Time Zone – US Eastern

    - UTC Offset –  -05 hours

    - Daylight Savings - Auto

MAIN MENU – TRACKS:

- SETUP

    - Wrap When Full – ON

    - Record Method – TIME

    - Interval – 00hrs 00 mm 05 sec

- PLEASE CLEAR OLD TRACKS BEFORE EACH FLIGHT!

CELL PHONES

Cell phone transmissions can interfere with GPS reception causing disruption (“spiking”) in the tracks.  Do not use your cell phone in the vicinity of goals where you may be scored by your track!

TURNING ON THE GPS LOGGER

The red button on the right side of the face of the unit is used to turn the unit on and off.  Occasionally a Geko unit will spontaneously shut off about 1 minute after it is switched on.  It is prudent to recheck the unit about two minutes after turning it on.  If it is still on there is not a problem.